## Slide 1: Robot Construction, Wiring, and Safety
SSI Robotics
September 7, 2013
Capitol College
Notes: Add topic slide: include that it concentrates on manual operation (i.e. tile-op)

## Slide 2: Agenda
Basic construction
  Build it strong
  Build it stable
  Build it to last
  Protect sensitive parts
Gearing
  Make motors do more
  Safety
Servos
  Safety
Wiring
  Make it reliable
Samantha
  Minimize ESD issues
Notes: Will this help students transition to C.

## Slide 3: Basic Construction
Build it strong
  Right angles are weak
  Triangles are strong
    Reinforce where necessary with angled supports
  Angles beams are stronger than flat beams
Notes: Will this help students transition to C.

## Slide 4: Basic Construction
Build it stable
  Keep the center of gravity low to keep the robot stable
Notes: Will this help students transition to C.

## Slide 5: Basic Construction
Build it to last
  Ran entire World Championship with NO major repairs required
    7 qualifiers
    4 eliminations
Notes: Will this help students transition to C.

## Slide 6: Basic Construction
Build it to last
  Tetrix kit comes with “kep” nuts
    These are ok but will loosen over time
  I recommend nylon lock nuts
    Much less likely to loosen up
      Note, they will wear out if removed and reinstalled many times
  Loctite is also useful to keep nuts where they belong
  Don’t use only the minimum number of screws
    One screw might hold, but 4 will hold it better
Notes: Will this help students transition to C.

## Slide 7: Basic Construction
Hint for axle collars
  Use a standard screw instead of the included set screw
  It will be easier to get a firm grip on the axle
Notes: Will this help students transition to C.

## Slide 8: Basic Construction
Protect sensitive parts
  Use plastic sheeting to protect electronics
    Mounting NXT, motor and servo controllers to plastic sheeting can help minimize effects of electrical noise
  Electronics make poor bumpers
  Mount the battery safely
    No sharp edges to cut into the battery
    A battery that shorts to the frame can cause major trouble
  Mount power switch so it is easy for the FTA to reach, but hard for another robot to bump
Notes: Will this help students transition to C.

## Slide 9: Basic Construction
Protect sensitive parts
  Make numbers out of a material that will withstand game play
    Laminated paper works well
    Laminated paper behind a plastic sheet works really well
    You don’t want them to tear off during a match
    Remember the 3” size is the Minimum (not maximum)
Notes: Will this help students transition to C.

## Slide 10: Gearing
Use gearing to make your robot work better
  Use gears between the motor and drive wheels
    Mounting the wheels directly to the motors makes it hard to get all wheels at the same level
    Gearing the wheels to the motor allows the wheel axles to be in a frame member which should make it easier to get all the wheels at the same level
Make your motors do more
  Gears are a force multiplier to allow a motor to do more work
  Make sure the gears mesh properly and all axels are properly supported
  Chain and sprocket systems can work the same as gears over a longer distance
Notes: Will this help students transition to C.

## Slide 11: Gearing
Gear safety
  Provide shielding if possible to prevent fingers or wires from getting caught in the gears.
  Using gearing to drive a mechanism too fast can be dangerous
    Treads can spin off of tires….
  Using surgical tubing along with gearing can make a motor’s job easier
    To help lift an arm
    To help pull in the legs of a scissors lift
Notes: Will this help students transition to C.

## Slide 12: Servos
Servo safety
  If you have servos that move during robot initialization, you MUST put a safety label by the power switch to indicate this. This is stated in the game manual <RG04> b
  Make sure the servo is mounted securely
    The old servo brackets were not very strong
    I have not seen the new options, they may be better
    We have made custom brackets out of 1” square aluminum tube
Notes: Will this help students transition to C.

## Slide 13: Wiring
Make it reliable
  The terminal blocks on the motor controllers are not very reliable for passing power to other controllers
  Use some type of terminal strip for more reliable power connections
  An example of using Anderson Powerpoles is available in the FTC document library (off of Team Resources)
  We have used a variation of this using an Anderson Powerpole splitter allowing us to have redundant connections to each controller
Notes: Will this help students transition to C.

## Slide 14: Wiring
Make it reliable
  Check wiring before and after EVERY match
    Last year at the World Competition, a robot was showing a low battery error on the Samantha during a couple of its matches (flashing red light)
    The battery was not low
    The problem was tracked down to a loose power connection to the Samantha
  Do not route wires where they will be damaged by robot mechanisms
    Be careful of rotating mechanisms that have motors on them
    Be careful of running wires too close to gears
    Be careful of pinch points
Notes: Will this help students transition to C.

## Slide 15: Wiring
Make it reliable
  Tie down all wiring
    If it is tied down, it can’t move into a pinch point
    It will be harder for another robot to get tangled up in your wiring
    Tie the motor power wires to the motor to keep them from coming loose
  Keep it neat
    This makes it easier to track down problems
    It will probably also impress the judges
Notes: Will this help students transition to C.

## Slide 16: Wiring
Make it reliable
  Don’t run power wires beside signal wires
    Motor or servo wires routed beside the I2C wires can induce noise on the I2C bus
    This can cause data errors
  Keep the USB cable from the Samantha separate from all other wires
    Use the shortest possible cable
    This should help prevent data errors on the USB bus
Notes: Will this help students transition to C.

## Slide 17: Samantha
Minimize ESD issues
  Mount the Samantha high and not surrounded by metal to allow a clean Wi-Fi signal
  Make sure all wire connections are tight and cannot move during match play
  Use a high quality shielded USB cable with ferrite chokes
  Add ferrite chokes, if needed to other wiring on the robot
Notes: Will this help students transition to C.